How to Update Falcon F110 Firmware using Device Discovery Tool

- Go to the F110 webpage at www.rletech.com to find the .upd file (UPD File) for the F110 firmware update.

- On the bottom left-hand side of the page you will find the Documentation/Files section.  Left click on the “UPD File” link and save it to your local drive.

- Once you have the F110 .upd file saved.  Open your RLE F110 Discovery tool and do a search for the F110 device(s) you need to update.  The F110 discovery tool is available for download at www.rleinfo.com, if you do not have your Product User Guide CD available.  You need to have a login name and password to access the RLE Info site.  A form is available on the site to register with RLE.

http://www.rleinfo.com/repsonly/pdf/RLE_F110_Discovery.exe

- First, left click on the F110 that needs to be updated, you will see the device highlighted.  Second, click on the UPDATE tab at the top of the discovery window.

- A warning will show after you select UPDATE.  It warns you to be sure the proper file is loaded to the F110 unit.  Loading an incorrect file type to the unit can possibly lock up the unit.

- A browser window will open after clicking the OK button.  Select the correct navigation path to where you have the .upd file stored for the F110 firmware update.

- You will be asked if you are sure about continuing with the firmware update after the file has been selected for upload.  The firmware upload process takes approximately one minute.  After the upload is completed, you will see a window prompt if you want to review the Update log.  The F110 firmware update is now completed

If you have any problems while updating the firmware on your Falcon F110, please contact RLE Technical Support by email (support@rletech.com), completing a tech support form (www.rletech.com), or by phone at (970) 484-6510 – select  “2”.